## Slide 1: Data Center Infrastructure CT109-3-2&Version 2
Fire Protection and Security Systems

## Slide 2: Topic & Structure of The Lesson
Fire Protection and Security Systems

## Slide 3: Learning Outcomes
At the end of this topic, YOU should be able to:
Explain the importance of fire regulations, how to prevent fire and identify the prime reasons for a fire suppression strategy.
Understand the various systems for fire detection, warning and fire suppression; including water, water-mist & gaseous suppressants. Identify how any system design needs to consider fire.

## Slide 4: Key Terms You Must Be Able To Use
If you have mastered this topic, you should be able to use the following terms correctly in your assignments and exams:
EFD
CO2
INERGEN

## Slide 5: Fire Risk
Only 20 percent or so of all fires start in the server room, or its environment. Nearly 80 percent of fires start outside IT structures. This risk therefore needs to be examined on two levels. Protection against fire originating in the server room can be covered by early fire detector systems (EFD), a fire-alarm and extinguishing systems.
These systems can also be designed redundantly – so that false alarms can be avoided. EFD systems suck ambient air from racks by means of active smoke extraction systems which detect even the smallest, invisible smoke particles.

## Slide 6
Due to high air speeds in climate-controlled rooms, the smoke is rapidly diluted, meaning that the EFD systems must have a sufficiently high detection sensibility.
Disturbances can be avoided or kept away with filters and intelligent signal-processing algorithms. Professional suppliers also offer these systems in a version that combines fire-alarm and extinguishing systems, which can be easily integrated in 19" server racks for space efficiency.

## Slide 7: Water Risk
An often neglected danger for IT systems is water. It is usually not a threat in the case of pipe leaks or floods, but represents a danger in the form of extinguishing water in the event of the above-discussed fire threats.
The damage caused by the fire is often less severe than the damage caused by the water used to extinguish it.

## Slide 8: Smoke Risk
Even if a fire is not raging in the immediate vicinity of a data center, smoke still presents a risk of severe damage to IT equipment. In particular, burning plastics such as PVC create poisonous and corrosive smoke gases.
Burning one kilogram of PVC releases approx. 360 liters of hydrochloric acid gas, producing up to 4500 cubic meters of smoke gas. This can destroy the IT facility in little time, a fact that reduces the "mean time between failure" (MTBF) substantially. MTBF is the predicted elapsed time between inherent failures of a system during operation.

## Slide 9: Power Supply Risk
Uninterruptible power supply systems, called UPS systems, take over when the power network fails. Modern UPS systems (online systems) operate continually, supplying consumers via their power circuits.
This means that the brief yet dangerous change-over time can be eliminated. The UPS system simply and reliably bridges the time until the power network is up and running again. Thanks to integrated batteries, UPS systems also operate continuously if power is off for a longer period of time.

## Slide 10: Explosion Risk
The risk of terror attacks or other catastrophes which could trigger an explosion must be factored in right from the start when planning a highly available security room concept.
Modern, certified server rooms need to undergo an explosion test. High-security modular server rooms are built with pressure resilient wall panels to resist heavy explosions, protecting valuable IT systems from irreparable damage. IT systems need also be protected against debris and vandalism, to ensure real all-round protection.

## Slide 11
"Experience tells us that a fire can break out at any given moment. When decades go by without a fire, it doesn't mean that there is no danger, it simply means that we have been lucky so far. Yet, the odds are still the same and a fire can still break out at any given moment."

## Slide 13: Room Concepts
The classical Room-in-Room Concept with separate technical and IT security rooms that house any type and number of server racks and network cabinets is equipped with raised floors, dropped ceilings if necessary, active and passive fire protection and a cooling system.

## Slide 14: Fire and Lightning
As lightning is one of the most common causes of fires, a lightning rod is mandatory in every data center building. In addition, responsible employees should provide all IT components with surge protection, to avoid the damage that can occur from distant lightning.
Structural measures can also be a help: When constructing a data center, some architects go so far as to use concrete that contains metal, so a Faraday cage is produced. This ensures that the IT infrastructure is well protected against lightning damage.

## Slide 15: Other Causes of Fires
Other causes are also associated with electricity; furthermore, overheating and explosions play an important role in connection with fire. Among other causes, fire that is started by electricity can erupt when the current strength or voltage of a power connection is too high for the device that is running on it.
Defective cable insulations also represent a danger, namely they provide sparks that can accidentally ignite inflammable materials that are located nearby.

## Slide 16: Fire Fighting (1)
Once a fire occurs, the data center infrastructure should already have the means to actively fight it. Sprinkler systems are especially important in this area. These are relatively inexpensive and are easily maintained, but are a problem in that the water can cause tremendous damage to IT components.
Apart from that, sprinkler systems provide only a few advantages when it comes to fighting concealed fires, like those in server cabinets or cable shafts.

## Slide 17: Fire Fighting (2)
CO2 fire extinguishing systems represent a sensible alternative to sprinkler systems in many environments. These operate on the principle of smothering burning fires, and therefore do not require water.
However, they also bring along disadvantages: For one, they represent a great danger to any individuals who are still in the room, and for another, they have no cooling effect, so they are unable to contain damage caused by the generation of heat

## Slide 18: Fire Fighting (3)
A further fire-fighting method is the use of rare gases. Fire extinguishing systems based on rare gases also reduce the oxygen content in air and thus suffocate flames.
However, they are less dangerous to humans than CO2, so individuals who are in the burning room are not in mortal danger. In addition, argon does not cause damage to IT products. Drawback: These systems are rather expensive.

## Slide 19: Surveillance Systems
Most of the points covered in the section on catastrophes, such as threats resulting from fire and water, only cause significant damage when they have the opportunity to affect IT infrastructures over a certain period of time.
It is therefore especially important to constantly monitor server cabinets, computer rooms and entire buildings, so that reaction times are extremely short in the event of damage.

## Slide 20: Conclusion
The possibilities for influencing the security of a data center security are by no means limited to the planning phase. Many improvements can still be implemented at a later point in time.
The implementation of rare gas fire extinguishing systems and high-performance systems for data center surveillance and access control were just two examples given in this regard.
It is therefore absolutely essential that those responsible for the data center continue, at regular intervals, to devote time to this topic and analyze the changes that have come to light in their environment, so they can then update their security concept to the modified requirements.

## Slide 21: Quick Review Question
Briefly explain three fire fighting methods that are being used in data centers.

## Slide 22
Summary of Main Teaching Points
Discussed the importance of fire regulations and explained fire detection, warning and fire suppression systems that includes including water, water-mist & gaseous suppressants.

## Slide 23: Question and Answer Session
Q & A

## Slide 24: What we will cover next
Building Automation and Energy Management Systems