## Slide 1: Mobile & Wireless Technology CT090-3-2 & Version 2
Radio Frequency Fundamentals for WLAN

## Slide 2: Topic & Structure of The Lesson
Radio Frequency (RF) Fundamentals for Wireless LAN Technology
Frequencies Used for Wireless LANs
Coverage and Capacity
Channel Reuse and Co-location
Basic Units of RF Measurement
RF Range and Speed
Environment: RF Behavior

## Slide 3: Learning Outcomes
At the end of this topic, You should be able to
Know the basic characteristics or properties of radio frequency.
Be familiar with the frequencies used for wireless networks.
Understand wireless network coverage and capacity.
Know what RF factors will affect the range and speed of wireless networks.
Identify basic RF units of measurement.

## Slide 4: Key Terms You Must Be Able To Use
If you have mastered this topic, you should be able to use the following terms correctly in your assignments and exams:

## Slide 5
Radio frequency (RF) plays an essential role in wireless LAN technology.
What is Radio Frequency?
RF is a Radio Frequency, a electromagnetic wave.
Radio waves/Radio Frequency waves/Electromagnetic waves are passed through the air (which is the medium) and are used to get information from one wireless device to another.
Radio Frequency Fundamentals for Wireless LAN

## Slide 6
How these Radio waves/Radio Frequency waves/Electromagnetic waves are generated?
High frequency alternating current (AC) signals passing over a copper cable connected to an antenna.
The antenna then transforms the signal into radio waves that propagate through the air from a transmitter to a receiver.
Radio Frequency Fundamentals for Wireless LAN

## Slide 7
Radio frequency (RF) waves are used in a wide range of communications, including
Radio
Television
Cordless phones
Wireless LANs, and
Satellite communication.
RF is around everyone and everything, and comes in many forms. Radio waves range from 3Khz to 300 Ghz.
Radio Frequency Fundamentals for Wireless LAN

## Slide 9
RF spectrum is governed by local regulatory bodies.
Location Regulation
Malaysia Malaysian Communications and Multimedia Commission(MCMC)
Canada ISC RSS-210
China RRL/MIC Notice 2003-13
Europe (ETSI) ETS 300.328
ETS 301.893
Israel MOC
Japan (MKK) TELEC 33B
TELEC ARIB STD-T71
Singapore IDA/TS SSS Issue 1
Taiwan PDT
USA FCC (47 CFR) Part 15C, Section 15.247
FCC FCC (47 CFR) Part 15C, Section 15.407
Radio Frequency Fundamentals for Wireless LAN

## Slide 10
The Wireless LAN(IEEE 802.11) standard addresses the 2.4 GHz ISM band and the 5 GHz UNII bands.
The 2.4 GHz ISM band allows for 11 of 14 channels to be used for wireless LAN communications.
The 5 GHz UNII band consists of three bands utilizing four frequency ranges.
The three bands are
UNII-1, the lower band;
UNII-2 and
UNII-2e
Frequencies used for Wireless LAN

## Slide 11
Coverage and capacity are two key factors to take into consideration when designing and implementing an IEEE 802.11 wireless LAN.
During the design phase of an IEEE 802.3 wired network, the design engineer will take capacity into consideration, verifying and validating that there are enough capacity switches, ports, etc., for the user base of the network.
Coverage and Capacity

## Slide 12
The term coverage has different meanings depending on the context in which it used.
For example, if you buy a gallon of paint, the label will specify the approximate coverage area in square feet.
If one gallon of paint covers 300 sq ft and the room you wish to paint is 900 sq ft, simple math shows at least three gallons of paint would be needed to effectively
cover the room.
The concept is similar in IEEE 802.11 wireless networks. However, unlike with paint, there is no simple rule that determines how much space an access point will cover with the RF energy it is transmitting.
Coverage and Capacity

## Slide 13
This coverage will depend on many factors,
some of which include:
1. Size of area –
The amount of area an access point will cover.
Manufacturer(ASUS/TPLINK) of wireless LAN hardware will not commit to
the amount of area an access point will cover.
A site survey of the area will help determine the coverage area of an access point.
2. Number of users –
The number of users in an area will also affect the RF coverage.
Too many users using powerful applications
will overload the access point, adding to the poor performance issues.
Coverage and Capacity

## Slide 14
3. Applications in Use –
The application types in use—either software or hardware—can affect the bandwidth of an access point.
If the users connected to an access point use bandwidth-intensive applications such as the CAD/CAM application mentioned earlier, this could result in poor throughput for all users connected to that access point.
Coverage and Capacity

## Slide 15
4. Obstacles, Propagation and Radio Frequency Range
  Obstacles in an area, such as walls, doors, windows, and furnishings, as well as the physical properties of these obstacles—thickness of the walls and doors, density of the windows, and type of furnishings—can also affect coverage.
  The radio frequency used—either 2.4 GHz or 5 GHz—will determine how well a signal will propagate and handle an obstacle.
Coverage and Capacity

## Slide 16
5. WLAN Hardware and Output Power
The wireless LAN hardware in use can also have
an impact on the coverage area.
Examples include the antenna type, antenna orientation,
and gain of the antenna.
The higher the gain of an antenna, the greater the coverage area; conversely, the lower the gain of an antenna, the smaller the coverage area.
The polarization of an antenna (horizontal vs. vertical) will also have an effect on the coverage area because of the different shapes of the radiation patterns.
Coverage and Capacity

## Slide 17
5. WLAN Hardware and Output Power
The output power of the transmitter or access point will also have an effect on coverage. The higher the output power, the greater distance a signal will propagate.
A higher power signal will provide more coverage.
Coverage and Capacity

## Slide 18
Just as an elevator or a restaurant has a limited number of people they can accommodate comfortably, wireless access points also have a capacity. The capacity of an access point is how many users the AP can service effectively, offering the best performance.
This capacity depends on several factors, including:
Software applications in use
Number of users
Basic Units of RF Measurement

## Slide 19
A wireless access point may be set to an output of 30 mW (milliwatts) of power. A milliwatt is 1/1000 of a watt.
Watts and milliwatts are measurements of RF power.
Other units of measurement for RF are dB, dBi, dBd, and dBm.
RF Range and Speed

## Slide 20
How far and fast an RF signal can travel depends on a variety of factors, including
line of sight,
interference,
Environment: RF Behavior
This section discusses these factors. RF communication between devices in 802.11 wireless networking requires a line of sight.
There are two types of line of sight to take into consideration: visual and RF.
RF Range and Speed

## Slide 21
Visual line of sight is the ability of the transmitter and receiver to see each other. In order for wireless networking direct link communication to be successful there should be a clear, unobstructed view between the transmitter and receiver.
An unobstructed line of sight means few or no obstacles blocking the RF signal between these devices.
RF Range and Speed

## Slide 22
The RF line of sight, or the radio transmissions between a transmitter and receiver, could be affected if the total area of radio frequency transmissions(the Fresnel zone )is blocked by more than 40 percent.
This blockage could be from a variety of sources such as trees, buildings, terrain, or other obstacles, including the curvature of the earth.
RF Range and Speed

## Slide 23
2. Interference from a radio frequency point of view occurs when a receiver hears two different signals on the same or similar frequencies. Interference causes distortion. In wireless LANs, this interference can have a severe impact on the quality of signal received by the wireless device.
IEEE 802.11 wireless network may use the unlicensed 2.4 GHz industrial, scientific, and medical (ISM) band. This band is also used for
many other devices, including:
Cordless phones
Microwave ovens
Medical devices
Industrial devices
Baby monitors
RF Range and Speed

## Slide 24
a. Co-channel and Adjacent Channel Interference
Co-channel or adjacent channel interference occurs when two devices in the same physical area are tuned to a close or same radio frequency channel. For example, an access point on channel 1 and another access point on channel 2 in close or hearing range of each other will experience adjacent channel interference.
RF Range and Speed

## Slide 25
b. WLAN/WPAN Interference
The performance of IEEE 802.11 wireless networks can be affected when they are co located with IEEE 802.15 wireless personal area networks or WPANs.
Bluetooth is an example of a personal area network. Like 802.11, Bluetooth devices operate in the 2.4 GHz frequency range and use frequency hopping spread spectrum (FHSS).
RF Range and Speed

## Slide 26
c. Bright Sunlight Interference
Bright sunlight will not affect wireless LAN communications that use the 2.4 GHz ISM and 5 GHz UNII bands;
RF Range and Speed

## Slide 27
3. Environment: RF Behavior
RF behavior is the result of environmental conditions including:
1. Reflection
2. Refraction
3. Diffraction
4. Scattering
5. Absorption
6. Diffusion
RF Range and Speed

## Slide 28
1. Reflection –
Reflection occurs when an RF signal bounces off a smooth, non absorptive surface such as a table top and changes direction.
Reflections can affect indoor wireless LAN installations fairly significantly in certain cases. Depending on the interior of the building—such as the type of walls, floors, or furnishings—there could be a large number of reflected signals.
If not properly handled, reflections could cause a decrease in throughput and poor network performance.
RF Range and Speed

## Slide 29
2. Refraction
When an RF signal passes between mediums of different densities, it may change speeds and also bend. This behavior of RF is called refraction. Glass is an example of material that may cause refraction.
When an RF signal comes in contact with an obstacle such as glass, the signal is refracted (bent) as it passes through and some of the signal is lost.
RF Range and Speed

## Slide 30
3. Diffraction
When an RF signal passes an obstacle, the wave changes direction by bending around the obstacle. This RF behavior is called diffraction. A building or other tall structure could cause diffraction, as could a column in a large open area or conference hall.
When the signal bends around a column, building, or other obstacle, the signal weakens, resulting in some level of loss.
RF Range and Speed

## Slide 31
4.Scattering
When an RF signal strikes an uneven surface, wave fronts of the signal will reflect off the uneven surface in several directions. This is known as scattering.
Scattering is another form of loss that may severely degrade the RF signal.
RF Range and Speed

## Slide 32
5.Absorption
When material absorbs an RF signal, no signal penetrates through the material. An example of absorption is the human body.
The human body has a high water content and will absorb RF signals. This type of absorption can be a problem for wireless network deployments in certain environments.
Densely populated areas such as airports and conference halls need to consider absorption when designing a wireless LAN deployment.
RF Range and Speed

## Slide 33: Quick Review Question
Coverage and capacity will depend on many factors. What are they? Explain each of them.
How far and fast an RF signal can travel depends on a variety of factors. What are they? Explain each of them.

## Slide 34
Summary of Main Teaching Points
This chapter looked at radio frequency basics and the essential role RF plays in the world of IEEE 802.11 wireless LANs. This chapter also looked at correct channel reuse to minimize interference from co-location of access points.
Coverage and capacity are two important areas that should be closely looked at in order to ensure a wireless deployment will offer reliable connectivity and perform well for the user base.
Finally, we discussed RF units of measure, including watt, milliwatt, dB, and dBi. We also looked at RF behaviors such as reflection, refraction, and absorption, and the impact of propagation on radio waves.

## Slide 35: Question and Answer Session
Q & A

## Slide 36: What we will cover next
WLAN Terminology and Technology
Wireless LAN Modes of Operation
Connecting to a Wireless Network
Distribution System (DS)
Data Rates, Throughput, Dynamic Rate Switching
WLAN Roaming