## Slide 1: Mobile & Wireless Technology CT090-3-2 & Version 2
WLAN Site Survey

## Slide 2: Topic & Structure of The Lesson
Gathering Business Requirements
Public Access, Hotspots, Hospitality
Interviewing Managers and Users
Manufacturer Guidelines and Deployment Guides
Defining Physical and Data Security Requirements
Gathering Site-Specific Documentation
Documenting Existing Network Characteristics
Identifying Infrastructure Connectivity and Power Requirements
Understanding RF Coverage and Capacity Requirements
Client Connectivity Requirements

## Slide 3: Learning Outcomes
At the end of this topic, You should be able to
Understand the business requirements of a WLAN.
Know various types of business models.
Understand the interview process.
Identify the importance of site-specific documentation
Know the importance of identifying existing networks
Be familiar with RF coverage requirements
Understand client connectivity requirements

## Slide 4: Key Terms You Must Be Able To Use
If you have mastered this topic, you should be able to use the following terms correctly in your assignments and exams:
Business requirements
Data security
Existing network infrastructure
Physical security
RF coverage
RF jamming
RF spectrum analysis
Site survey
Wiring closet

## Slide 5
Gathering Business Requirements
Gathering information is typically the first step of a wireless LAN design and implementation. As mentioned, the business model or type of business where the wireless LAN will be deployed is a major part of deciding the level of a wireless LAN site survey.
The type of business will determine the needs and use of a wireless network. Knowing the applications used—both hardware and software—is a critical part of a wireless LAN deployment as this will affect recommendations such as the number and locations of access points.
Expectations can make or break a wireless LAN deployment.

## Slide 6
Public access, hotspots, and hospitality may need to accept connections from a wide variety of client devices, including IEEE 802.11b/g and 802.11a devices.
In many cases, consumer brand notebook computers will be limited to 802.11b or 802.11b/g technology. Backward compatibility to these technologies is essential because the infrastructure will have no control over the type of client device that may connect.
If backward compatibility is not taken into consideration, some devices may not be able to connect and use the wireless network.
Public Access, Hotspots, Hospitality

## Slide 7
Understanding the intended use of a wireless LAN is a critical part of a successful deployment.
Who better to explain what the wireless network will be used for than those who
will be using it? Those performing a site survey may not necessarily understand the functional aspects of a certain type of business, therefore it is critical to get input from all who will be using the wireless network.
Department managers, team leads, and business unit managers usually know the function of their specific areas of the organization the best. Therefore they will also know the needs and requirements of users of the wireless network and how a successful deployment will help increase job productivity.
Interviewing Managers and Users

## Slide 8
The information just presented includes some types of questions that need to be addressed during the site survey process. Keep in mind that the actual questions and details are dependent upon the business model and the implementation of the wireless network.
Check with the specific manufacturer of the equipment to be used for site survey guidelines and deployment guides. These will provide additional information that is helpful in generating a list of questions and concerns that will need to be addressed.
Manufacturer Guidelines and
Deployment Guides

## Slide 9
Understanding the security requirements of both the physical environment and the user data is another design aspect of a wireless network. Because wireless LANs use RF to send and receive information such as computer data, wireless LANs are vulnerable to something known as RF jamming, which is caused by RF interference and can be either intentional or unintentional.
As the name implies, RF jamming disrupts RF communications. If an intruder wants to wreak havoc in a wireless network, they can use an RF signal jammer
to cause interference on the same RF bands used by the wireless network. The only way to protect against this kind of activity is through physical security.
Defining Physical and Data Security
Requirements

## Slide 10
Physical security includes blocking RF signals from either entering or leaving a location. This could be done in a variety of ways—shielding materials can include metal, paint, or even wallpaper. If physical security is a concern where the wireless network will be installed, this needs to be taken into consideration during a site survey and design stages.
Data Security - Due to situations beyond their control, some organizations ensuring that information such as computer data is received by the intended recipients without tampering during transit.
Defining Physical and Data Security
Requirements

## Slide 11
Documentation for the location where a wireless network will be installed will make a surveyor’s job much easier and result in a better overall deployment. Drawings and other documentation pertaining to the following list can provide valuable information:
Floor plans
Blueprints
Proposed location of furnishings
Electrical specifications
Gathering Site-Specific Documentation

## Slide 12
Documentation for the location where a wireless network will be installed will make a surveyor’s job much easier and result in a better overall deployment. Drawings and other documentation pertaining to the following list can provide valuable information:
Floor plans
Blueprints
Proposed location of furnishings
Electrical specifications
Gathering Site-Specific Documentation

## Slide 13
Documentation is a major part of any business, and computer networks are no exception.
In order to have a successful deployment of a wireless network, it is critical to know the details of the existing network infrastructure as well as future implementations, upgrades, and modifications.
These existing infrastructures may include a wired or wireless network already in place and functioning that may be upgraded or in a new deployment.
Documenting Existing Network Characteristics

## Slide 14
Existing wireless networks The questions that are asked regarding the existing wireless network will help determine the role it is going to play. If the existing network is going to remain in place, understanding its technical details and how to work it into the design of the new or upgraded deployment will help create a successful and productive wireless LAN deployment.
Existing wired networks In addition to knowing of any existing wireless networks, it is also important to know about the wired network infrastructure. Any existing documentation on the wired network infrastructure will help streamline the process for connecting in the wireless components of the network.
Documenting Existing Network Characteristics

## Slide 15
Network infrastructure connectivity plays a big role in wireless networking. A wireless LAN site survey will require additional information about the network infrastructure and power requirements. In a sense, a wireless site survey also requires a wired or infrastructure survey.
Some of the information regarding the wired network includes:
Location of wiring closets
Wired infrastructure network devices in use
Connection speed between sites
Electrical power requirements
Identifying Infrastructure Connectivity
and Power Requirements

## Slide 16
Network infrastructure connectivity plays a big role in wireless networking. A wireless LAN site survey will require additional information about the network infrastructure and power requirements. In a sense, a wireless site survey also requires a wired or infrastructure survey.
Some of the information regarding the wired network includes:
Location of wiring closets
Wired infrastructure network devices in use
Connection speed between sites
Electrical power requirements
Identifying Infrastructure Connectivity
and Power Requirements

## Slide 17
Radio frequency range of the network to be installed
Wireless LAN hardware to be used
Output power of the transmitters
Receive sensitivity of the receivers
Understanding RF Coverage and
Capacity Requirements

## Slide 18
Client devices that will be connecting to the wireless LAN also need to be considered as part of a site survey. This includes knowing the radio type, antenna type, gain, orientation, portability, and mobility of the device. Understanding the type and function of client devices will have an impact on the design of the wireless network.
Common wireless client devices include:
Notebook computers
PDAs
Pocket computers
Barcode scanners
Client Connectivity Requirements

## Slide 19: Quick Review Question
Define Physical security.
Define Data security.

## Slide 20
Summary of Main Teaching Points
In this chapter, we discussed the business aspects of wireless LAN site surveys.
This chapter also discussed the importance of gathering information as well as the type of information required to successfully perform a wireless LAN site survey and design of a wireless network.
This chapter also discussed taking into consideration the physical and data security requirements of the wireless network.
This chapter discussed RF coverage requirements and the factors to be taken into consideration to ensure proper coverage throughout the location where the wireless network is installed. Finally, client connectivity requirements and other considerations were discussed.

## Slide 21: Question and Answer Session
Q & A

## Slide 22: What we will cover next
Troubleshooting and Maintaining Wireless Networks
Identifying Wireless LAN Problems
Software and Hardware Upgrades
Optimizing Wireless Networks
Infrastructure Hardware Selection and Placement
Identifying, Locating, and Removing Sources
of Interference
Client Load Balancing
Analyzing Infrastructure Capacity and Utilization