## Slide 1: System and Network Administration
Network Hardware
Virtual ethernet interfaces

## Slide 2: Network Devices
Load balancer
Switch
Firewall
Router
Proxy

## Slide 3: Switches
Creates dedicated connections involving only two hosts in a transmission.
Sends individual packets to specific destination host based on their physical (MAC) addresses.
Security protections provided by switches:
  Can limit access to specific ports based on MAC address.
  Can implement flood guards to protect against DoS attacks.
  Can implement loop prevention to shut down network loops.
Switch: A device with multiple network ports that combines multiple physical network segments into a single logical network.

## Slide 4: Routers
Router can filter network traffic through ACLs and block unwanted traffic.
One type of Firewall technique
Router: A device that connects multiple networks that use the same protocol.
Access control list: A set of rules for blocking or allowing traffic.
Can determine most efficient path for network traffic to take.
Most routers will not forward broadcast traffic.

## Slide 5: Proxy
Used as a way to filter content.
Forward proxies intercept client traffic before it leaves the internal network.
Reverse proxies intercept traffic coming from an external network.
  Intended to protect destination servers from compromise.
Proxies can modify traffic or just forward it.
Some proxies are multi-purpose and have application-level awareness.
A device that acts on behalf of one end of a network connection when communicating with the other end of the connection.

## Slide 6: Firewall
Predefined rule sets (ACLs) determine what traffic to block.
Connection information can be saved to a log for monitoring.
Types of firewalls:
  Host-based
  Network-based
  Web application
Firewall: A device that protects a system or network by blocking unwanted traffic.
Load Balancer: A device that distributes traffics to various servers to balance CPU and memory use

## Slide 7: Network Address Translation
Offers simple security by concealing internal addresses from the Internet.
Packets sent by router to the Internet appear to come from the public address.
A service that translates between different IP addressing schemes, such as between public and private IP addresses.
NAT Router
24.213.151.4
192.168.12.20
192.168.12.30
192.168.12.100
Public IP address
Private IP address

## Slide 9: Virtual ethif
Virtual interfaces allows you to use multiple IPs on a single physical network interface
The main advantage is that you don’t need to have a physical adapter for each IP, but instead you can create multiple virtual interfaces (aliases) for a single physical card.
Done to allow webservers to host multiple SSL encrypted web sites on a single webserver, or to allow VPNs to communicate on a dedicated IP address
Two primary means of creating virtual IPs on a Linux host:
  Ifconfig
  iproute2

## Slide 10: Virtual ethif - ifconfig
Assuming that the interface being used is eth1, This command will create a virtual interface for eth0 with a name of eth1:0
ifconfig eth1:0 192.168.1.28
This command creates an apparent separate device from eth1 with it's own IP address, netmask, and broadcast address.
no gateway – usually only one gateway per machine.
To remove it use ifconfig with the down option for the device:
ifconfig eth1:0 down

## Slide 11: Virtual ethif - ifconfig
Update the routing table using arping, to bind the physical interface MAC to the virtual interface IP address
arping -q -U -c 3 -I eth1 192.168.1.28
This can now be used to host services and servers, fielding connections to clients or other hosts.
These changes made will be lost when the machine is rebooted.
  Add the commands to the network up and down scripts

## Slide 12: Virtual ethif - iproute2
The iproute tool set is tremendously powerful: one can easily perform complex tasks on the network stack of any Linux host with this tool
Its power is its great flexibility, and with great flexibility comes great complexity - however, it has particular advantages for managing virtual interfaces
The description of the ip command from the man pages describes this suite well:
ip - show / manipulate routing, devices, policy routing and tunnels

## Slide 13: Virtual ethif - iproute2
To create a virtual interface
ip addr add 192.168.1.28 dev eth1
To see all IP addresses that are assigned to an interface
ip addr show dev eth1
Or leave off dev ethN to get the same for all interfaces on the system (it is not possible to do this with ifconfig)
To remove the virtual interface
ip addr del 192.168.1.28/32 dev eth1
Note that the device must be specified when creating and deleting. While the subnet mask may be specified for the deletion, it is not required.